## Slide 1: Argus Realistic Target Coverage with Drones
Ahmed Saeed, Ahmed Abdelkader, Mouhyemen Khan, Azin Neishaboori, Khaled Harras, and Amr Mohamed

## Slide 2: Target Coverage Problem
Given the location of a set of targets, find the best camera configuration to cover them
Assumes known target information and camera parameters

## Slide 3: Sources of Target Information
  Applications: surveillance, cinematography, and infrastructure inspection
  Coarse grain coverage Fixed target configuration

## Slide 4: Constraints for Target Coverage
Camera Field of View Rmin, AOV, and Rmax
Target Size A target is covered only if all of it is in the camera’s view
Viewing Direction Target and camera facing each other
Occlusions Mutual occlusion between targets and occlusion because of obstacles

## Slide 5: Status of Target Coverage Algorithms
Targets typically represented as points overlooking target size, orientation and occluders
Sensor capabilities (e.g., coverage area, energy constraints, and connectivity)
  Coverage of point targets using fixed PTZ cameras [INFOCOM’11,’12]
  Heuristics for coverage with mobile cameras [MASS’14 and MobiWac’14]
Quality of coverage (e.g., location of targets within camera field of view)
  High quality coverage of targets using fixed PTZ cameras [INFOCOM’14]

## Slide 6: But targets are more than blips on the radar …

## Slide 7: Outline
A Realistic Target Model
Argus System Architecture
New Algorithms for a New Model
Experimenting with Argus
Conclusion

## Slide 8: Realistic Target Model Oriented Line Segment Model
Targets have width, orientation, and location
Targets parameters can be captured by line segments
  Line segment length represents width
  Vector perpendicular to line segments represents orientation

## Slide 9: Coverage Model
A target is covered if
  Facing the camera
  Not occluded by other objects
  Fully contained in the field of view of the camera (avoid stitching)

## Slide 10: Outline
A Realistic Target Model
Argus System Architecture
New Algorithms for a New Model
Experimenting with Argus
Conclusion

## Slide 11: Argus
Two-tier surveillance system
Top tier: coarse grain surveillance
  Count, location, and width
Bottom tier: fine grain information
  Facial and activity recognition

## Slide 12: Argus
Oriented Line Segment Coverage (OLSC) Solver
Finds cameras location and orientation to cover all targets
Minimizes the number of cameras needed to cover all targets
  Problem is NP-Hard and APX-Hard
  O(log N) approximation is best possible

## Slide 13: OLSC Solver
Approach: reduce OLSC to a set cover instance
Finds the best configuration of drones to cover targets
  Spatial Discretizer
  Angular Discretizer
  Configuration Selector

## Slide 14: OLSC Solver
Approach: reduce OLSC to a set cover instance
Finds the best configuration of drones to cover targets
  Spatial Discretizer
  Angular Discretizer
  Configuration Selector

## Slide 15: OLSC Solver
Approach: reduce OLSC to a set cover instance
Finds the best configuration of drones to cover targets
  Spatial Discretizer
  Angular Discretizer
  Configuration Selector
x
x
x

## Slide 16: OLSC Solver
Approach: reduce OLSC to a set cover instance
Finds the best configuration of drones to cover targets
  Spatial Discretizer
  Angular Discretizer
  Configuration Selector
x
x
x
x

## Slide 17: Outline
A Realistic Target Model
Argus System Architecture
New Algorithms for a New Model
Experimenting with Argus
Conclusion

## Slide 18: Spatial Discretizer
Converts the infinite search space into a few representatives
Selects representatives that can represent any optimal configuration
Comprehensive representation necessary for approximation algorithm

## Slide 19: How to Cover a Single Target?
Rmax
Target has to be within range of the camera

## Slide 20: How to Cover a Single Target?
Rmax
Target has to be facing the camera

## Slide 21: How to Cover a Single Target?
Target has to be fully contained the cameras view

## Slide 22: How to Cover a Single Target?
Camera should be facing the target within a certain viewing angle for quality of view

## Slide 23: How to Cover a Single Target?
We call this shape the Basic Camera Placement Field (BCPF)

## Slide 24: How to Cover a Single Target?
Exclude occlusion areas from BCPF
Excluding more areas based on any arbitrary constraints does not affect the rest of our approach

## Slide 25: How to Cover a Pair of Target?
Two targets have to be within the angle of view (AOV) of the camera
AOV circles

## Slide 26: Spatial Discretizer
Representatives generated by intersecting CPFs and AOV circles
Constraints enforced in pairwise fashion for N targets
Comprehensive representation is possible but requires O(N4)
  Comprehensive representation allows for O(log N) approximation
Heuristic: sample the BCPF at a small fixed angle
  Works surprisingly well and is only O(N)

## Slide 27: Angular Discretizer
Selects viewing directions for each representative
Chosen angle can be adjusted to put targets at the center of the field of view or other objectives

## Slide 28: Configuration Selector
Discretizers produce candidate camera configurations each covering a subset of targets
  Camera configurations Sets
  Targets
  Minimize number of cameras to cover all targets
Greedy algorithm provides O(log N) approximation for OLSC
  Set Cover
  Elements

## Slide 29: Outline
A Realistic Target Model
Argus System Architecture
New Algorithms for a New Model
Experimenting with Argus
Conclusion

## Slide 30: Argus Implementation
An autonomous system of drones
Central controller
  Drone and target localization
  Drone autonomous control
Drones process images locally
Sensors array and processor added to each drone to improve control and add computational capacity

## Slide 31: Demo
https://www.youtube.com/watch?v=KJbZWtGehPg

## Slide 32: Overhead of OLSC Solver
Processing time is dominated by the control overhead of two drones
One drone
Two drones

## Slide 33: Conclusion
We presented a more realistic target model that enables a new class of target coverage algorithms
The Oriented Line Segment model is flexible enough to allow different coverage constraints and desired quality objectives
Proposed heuristic is suitable for realtime application including surveillance and cinematography

## Slide 34: Questions? Ahmed Saeed: amsmti3@gatech.edu